## Slide 1: Efficient Matrix Multiplication on FPGAs
Sixiao Zhu, Jiali Jiang, Wenqiang Wang, and Ningyi Xu, MSRA
February 3, 2016

## Slide 2: Introduction
BLAS (Basic Linear Algebra Subprograms) is fundamental to most computations in scientiﬁc applications
  BLAS Level1: Dot-product, O(N)
  BLAS Level2: Gaxpy, Matrix*Vector, O(N2)
  BLAS Level3: GEMM, Matrix*Matrix, O(N3)
GEMM is important
  Heavily used in image/speech recognition, and many other machine learning applications
  Using MM to calculate CNNs has been adopted by many DL libraries (cuDNN, Caffe)
Goal: a scalable, highly efficient FPGA BLAS library (fBLAS) for various users
End User | Programming Language | fBLAS library format
SW programmers who want to use Catapult FPGA | C++/CUDA/OpenCL | cuBLAS-like API and .lib
FPGA programmers | OpenCL | OpenCL source code
RTL designer | Verilog/VHDL/A++ | A++ source code/generated RTL
Notes: GAXPY: General matrix A multiplied by a vector X plus a vector Y.

## Slide 3: OpenCL-based implementation
Approach: single work-item style
Benefits
  Easy to use by software programmers (OpenCL APIs)
  Easy to be integrated to OpenCL-based FPGA projects
  Scalable (e.g. DSP numbers, matrix size, tile size) and flexible (e.g. floating point -> fixed point)
Challenge: fine-grained control of generated circuits with OpenCL
Hardware structure
  Fully pipelined, tile-based structure
  Efficient adder tree
  Ping-pong buffer
Notes: 1.9x over Intel’s MKL (Math Kernel Library), better than Altera lib in area/perf, etc

## Slide 4: OpenCL fBLAS GEMM performance results
fBLAS/Altera MM
  Catapult Pikes Peak
  Altera SDK for OpenCL, 64-Bit Offline Complier, Version 15.1.0 Build 185
  42.9 GFLOPS
MKL
  Intel Xeon E5620(@2.40GHz) 4 Core 4/8 Threads, Intel compiler version 16.0, MKL version 11.3
  22.5 GFLOPS/31.4 GFLOPS
Chart: Performance Comparsion
| 128 | 256 | 512 | 1024 | 2048 | 4096
fBLAS | 0.5 | 1.4 | 8.3 | 56.6 | 419.7 | 3208.4
Altera Example | 0.6 | 1 | 8 | 63 | 522 | 4215
MKL | 0.4 | 2.3 | 15 | 81 | 760 | 6097
fBLAS_fix | 1 | 4.1 | 21.7 | 133.4 | 927.9

## Slide 5: OpenCL fBLAS GEMM performance results
Chart: Performance Comparsion
| 128 | 256 | 512 | 1024 | 2048 | 4096
MKL | 1 | 1 | 1 | 1 | 1 | 1
Altera Example | 0.66667 | 2.3 | 1.875 | 1.2857 | 1.4559 | 1.4465
fBLAS | 0.8 | 1.6429 | 1.8072 | 1.4311 | 1.8108 | 1.9003
fBLAS_fix | 2.3 | 3.6585 | 3.7327 | 5.6972 | 6.5708
Notes: Microsoft Catapult FPGA accelerating card with Altera Stratix V D5 FPGA
A single memory channel to the on-board 4GB of DDR3 memory (512M x 72b + ECC, 800MHz bus), exposing an Avalon bus interface operating at 200 MHz
ALM: 121990 / 172600 (71 %)
RAM bits: 11810950 / 41246720 (29 %)
DSP: 136 / 1590 (9 %)
Altera SDK for OpenCL, 64-Bit Offline Complier, Version 15.1.0 Build 185

## Slide 6: OpenCL implementation bottleneck
Bottleneck
  ALMs: ‘reduction operation’ in dot-product (sum up 128 float)
    Compiler generates human unreadable Verilog code
  Current version makes use of 128 DSP (total: 1590) because of the ALM limitation, 8.5% DSP uses up 71% logic resource
Solution(s)
  OpenCL: more resources (256 DSP version coming soon), optimized reduction operation
  A++: generates the same Verilog code with AOC
  Verilog HDL:
    Utilize all DSPs: 10x in peak GFLOPS, bottleneck will be DDR3 BW
    Customized floating point unit
 | Coding Style | RAM bits (41,246K) | ALMs (172K) | DSPs (1590) | DDR3 BW | Performance (4096x4096)
fBLAS (OpenCL) | Single workitem | 11,810K (29 %) | 122K (71%) | 136 (8.5%) | 2GBps (25%) | 42.9 GFLOPS
Altera M*M OpenCL | Multiple workitem | 10,952K (27%) | 166K (96%) | 264 (17%) | 1.54GBps (18.4%) | 33.0 GFLOPS
M*V (by Srinidhi Kestur, John Davis, Eric S. Chung) | Verilog, Xilinx V6-LX240T, 32PE | 63% | 71% | 56% | 80% | 1.14 GFLOPS

## Slide 7: Limitations by now: Resource
Resource consumes heavily on reducing operation in dot product (128 float points sum up in one cycle).
Compiler generates human unreadable Verilog code.
Current version makes use of 128 DSP (totally 1590 on board) because of the ALM limitation, 9% DSP uses up 71% logic resource.
 | Coding Style | RAM bits | ALMs | DSPs | Performance (4096x4096)
fBLAS (OpenCL) | Single workitem | 11,810K (29 %) | 122K (71%) | 136 (8.5%) | 1.3x
Altera MM OpenCL example | Multiple workitem | 10,952K (27%) | 166K (96%) | 264 (17%) | 1

## Slide 8: Structure and major techniques
X
X
X
X
+
+
+
FIFO
FIFO
Kernel for DDR read
Kernel for fp operation and accumulate
+
Tile A (four banks)
Tile B (four banks)
DDR3 on Catapult
DDR Read
DDR Write
accumulate
Register array
Dot product unit

## Slide 9: Basic strategy: Do the calculation by tile

## Slide 10: Basic strategy: Why tiling?
The idea of data locality.
In matrix multiplication, data is reused (data is , float point operation is ), thus refetched. We want to fetch data from block RAM rather DDR.
Suppose we have matrix A: , matrix B: .
Without tiling:
With tiling:

## Slide 11: Further improve DDR Read with Asynchronous IO
Decompose IO and computing: kernel 1 for DDR reading and kernel 2 for computing.
K1 and K2 are connected with a deep FIFO, with push and pop ports width ratio 1:4.
K1 reads a tile from DDR, pushes it into the deep FIFO with low bandwidth.
K2 pops the tile from the FIFO, with high bandwidth, and compute.
Resulting: K2 is computing current tile, while K1 is pushing into the next tile. In fact a implicitly Ping-Pong.
Reduces 75% IO time consume.

## Slide 12: A simple performance analysis
128 DSP, tile size 64 float, FIFO port ratio 1:4 (64 float per cycle at computing kernel side)
IO overhead , bottleneck lays on number of computing units, (Or practically, board resource).

## Slide 13: A simple performance analysis
The computing intensive part is fully pipelined, performance is highly predictable.
Chart: Performance Comparison
| 128 | 256 | 512 | 1024 | 2048 | 4096
experiment | 0.5 | 1.4 | 8.3 | 56.6 | 419.7 | 3208.4
theoretical | 0.2 | 1.2 | 7.5 | 52.4 | 388 | 2978

## Slide 14: Optimization detail: Improve local bandwidth
128 DSP means on chip storage system must feed 128 + 128 floats to the multipliers.
How to provide the high local bandwidth? Banking + Dual port reading.
Banking: One bank for one column, for reading one row per cycle from FIFO to local RAM.
  #pragma unroll
  for (int c = 0; c < TILE_SIZE; ++c)
  tile_b[r][c] = tmp[c];
Dual port reading: Make compiler infer dual port RAM.
  float2 tmp = (float2)(tile_b[r][c], tile_b[r + 1][c]);

## Slide 15: Optimization detail: Asynchronously transpose
Matrix A and B are stored row major, but in matrix multiplication, rows of A dot product columns of B.
Tile B need to be transposed, we want O(1) transpose.
Difficulty: tile B is banked stored, one bank per column, for storing one row per cycle. So we can not fetch an entire column in one cycle.

## Slide 16: Optimization detail: Asynchronously transpose
How to solve this?
We use this computing order: We fetch out one column of tile B to dot product all rows of tile A.
So every fetched column of B will be reused for times.
So, during this 32-cycle computing, we prepare the next column of tile B with a low-bandwidth manner, that is, fetching elements of the next B column in the same bank.

## Slide 17: Optimization detail: Asynchronously transpose
Substitute
Channel B
Dual port read
Four banks
Current column
Next column

## Slide 18: Optimization detail: Stall free pipeline at critical region
Advantage of HLS: Auto pipelining.
Consider the following code, this is the compute intensive portion of the MXM.
  for (int i = 0; i < TILE_SIZE; ++i) {
  for (int j = 0; j < TILE_SIZE; ++j) { // one B_column for all A_row
  result_i_j = dot (tile_A_row_j, tile_B_column_i);
  accu[i][j] += result_i_j; // [1] may exists write after read problem
  }
  }
  At the compiler’s perspective, Resign [1] may exists data dependency risk, so it generates hardware that executes serially (stall the pipeline) at this region.
  Yet at the programmer’s perspective, there is no such dependency cause we know the logic.

## Slide 19: Optimization detail: Stall free pipeline at critical region
Shift trick:
  #pragma unroll
  for (int i = 0; i < L - 1; ++i) {
  sh[i] = sh[i + 1];
  }
  accu[ndx - (N_SH - 1)] = sh[0];
  sh[N_SH - 1] = accu[ndx] + sum;
We explicitly tell the compiler to shift load and store operation on the same BRAM index by an amount of cycles.
Making place for the compiler to generate the pipelined hardware, as while meeting our semantics.

## Slide 20
substitute
Channel B
Channel A
+
Dot product
Dual port read
Accumulating tile
Batch IO
Batch IO
Current tile B column
Next tile B column
Shifting queue to solve load/store dependency
Four banks
Tile multiplication and accumulation pipeline

## Slide 21: Altera OpenCL experience
Altera’s OpenCL compiler provides little primitives, design purpose is inferred by coding style. Subtle tricks are needed for generate the design we want.
We summarized these experiences into a write paper.

## Slide 22: Altera OpenCL experience: Example
Inferring a register array
reg[SIZE];
#pragma unroll
for (int i = 0; i < SIZE; ++i) {
reg[i] = 0;
}
Inferring a bank interleaved block RAM array
banked_bram[SIZE][SIZE]
for(int i = 0; i < SIZE; ++i) {
#pragma unroll
for (int j = 0; j < SIZE; ++j) {
banked_bram[i][j] = 0;
}
}

## Slide 23: Future work
fBLAS
  BLAS library written in OpenCL/A++
  Usage
    APIs to SW
    Invoked by higher level compilers ()
Evaluated on Dragontail Peak

## Slide 24
Thanks

## Slide 25: 3rd-level BLAS (Basic Linear Algebra Subprograms)
3rd–level BLAS stands for matrix multiplication:
Useful in accelerating convolution operation in CNNs
  Many deep learning library like cuDNN and Caffe have adopted this approach.

## Slide 26: A FPGA MM library: fBLAS
Achieves up to 90% performance advantage over Intel’s Math Kernel Library.
Better than Altera provided example on:
  Saving resources: 30% performance promote with half DSP usage and about 20% logic resource usage.
  Single workitem, easier to be integrated into other applications.
  Performance predictable
  Fully pipelined, maxing the hardware’s computing capacity

## Slide 27: Related work
John David
FPGA BLAS
cuBLAS
MKL